## Slide 1: Airfoil Design Optimization
Andrew Smith
BS/MEng in Mechanical Engineering

## Slide 2: Project Overview & Agenda
Problem Definition
Proposed Solution
Learning Algorithms
Results & Visualization
Geometry Comparison
Areas for Investigation

## Slide 3: Problem Definition
How do we pick an airfoil shape that is best suited for a specific application?
Importance:
Air-travel accounts for ~2.5% of global CO2 emissions.
Demand for air-travel has increased from 1.6 billion to 5.0 billion passengers annually between 2000 and 2024.
Optimized airfoil geometry can reduce fuel expenditure by 20 to 25%.
Notes: Applications in wind turbines
Applications in biology

## Slide 4: Proposed Solution
Use Reinforcement Learning!
Create a custom gym environment for generating, simulating, and evaluating airfoil geometries.
Allow RL agents to act on the environment and search for an optimal solution.

## Slide 5: Proposed Solution - Environment & Agents
Initialize:
Setup observation space
Setup action space (8D continuous)
Initialize state (symmetric airfoil)
Step:
Apply action to state
Generate airfoil geometry (bezier curves)
Evaluate geometry (XFOIL)
Calculate reward (L/D ratio)
Render:
Not used
Reset:
Resets to initial state
Soft Actor-Critic (SAC):
Off policy
Continuous action space
Model free
Stochastic
Deep Deterministic Policy Gradient (DDPG):
Off policy
Continuous action space
Model free
Deterministic

## Slide 6: Proposed Solution - 4-Digit NACA vs. Bezier Parameterization
4-Digit NACA:
1st digit: maximum camber as a percentage of the chord length (f/c).
2nd digit: Location of maximum camber along the chord line from the leading edge (xf/c).
3rd and 4th digits: Maximum thickness as a percentage of chord length (t/c).
Bezier Curve Parameterization:
Upper and lower surfaces defined by control points.
For this project:
  8 control points
  x-position fixed
  y-position varies
  8D continuous action space
Notes: National Advisory Committee for Aeronautics (NACA)

## Slide 7: Proposed Solution - Evaluate Using XFOIL
What is it?
Developed in the 1980s by Mark Drela, XFOIL is a computational fluid dynamics (CFD) software that evaluates performance metrics of 2D airfoils.
Inputs:
Airfoil geometry (.dat file)
Angle of attack (5-7 deg)
Reynolds number (1.0e6)
Iterations (250)
Outputs:
Lift coefficient (CL)
Drag coefficient (CD)
Challenges:
Simulation runtime (~1.5s per sim)
Does not always converge
Prone to crashing
Bad Geometry
Self Intersection
Notes: 2-5 cruising
~7 climbing
10-12 landing/takeoff
15-20 stall

## Slide 8: Proposed Solution - Evaluate Using XFOIL
How XFOIL calculates performance metrics:
Discretize the space and solve using Finite Element Methods (FEM)

## Slide 9: Proposed Solution - Environment
Initialization:
Action Space:
  ± 0.15 for 8D space.
Observation Space:
  0.05 to 0.15 for upper leading point
  -0.15 to -0.05 for lower leading point
  ± 0.15 for all other points
Initial State:
  0.1 for upper points
  -0.1 for lower points
  L/D: 24.24
Step:
Apply action and update state (clip to observation).
Check for simulation stability
  If self intersection or points too close (0.025):
    Do not run simulation
    Reward = 0
  Otherwise:
    Reward = average L/D ratio

## Slide 10: Learning Algorithms
Soft Actor Critic (SAC)
Deep Deterministic Policy Gradient (DDPG)

## Slide 11: Learning Algorithms
Soft Actor Critic (SAC)
Learning starts: 512*
Batch size: 128*
Learning steps: 4096*
SB3 wrapper used to implement
Deep Deterministic Policy Gradient (DDPG)
Learning starts: 1024*
Batch size: 128*
Learning steps: 4096*
SB3 wrapper used to implement

## Slide 12: Results & Visualization - Convergence
Soft Actor Critic (SAC)
Deep Deterministic Policy Gradient (DDPG)
L/D Ratio: 121.59
L/D Ratio: 66.72

## Slide 13: Results & Visualization - Convergence
Soft Actor Critic (SAC)
Deep Deterministic Policy Gradient (DDPG)
Gradual Stochastic Convergence
Sudden Deterministic Convergence

## Slide 14: Geometry Comparison
Soft Actor Critic (SAC)
(L/D: 121.59)
Deep Deterministic Policy
Gradient (DDPG)
(L/D: 66.72)
NACA 6409 Airfoil
(L/D: 144.85)
SG6043 Airfoil
(L/D: 128.79)
Notes: Selig / Giguere for wind turbines

## Slide 15: Areas for Investigation
Control Points:
Spacing
Degrees of freedom
Action and Observation Constraints:
Upper bound
Lower bound
Loosen/tighten constraints
Hyperparameter Tuning:
Batch size
Learning starts
Learning steps
Simulation Parameters:
Angle of attack
Reynolds number
Iterations
Optimization Strategy:
Proximal Policy Optimization (PPO)
Twin Delayed Deep Deterministic Policy Gradient (TD3)
Geometric Parameterization:
NACA 4-digit
Class-shape transformation (CST)
Parametric equation concept (PARSEC)

## Slide 16: References
https://doi.org/10.1016/j.ast.2025.110638
https://doi.org/10.1038/s41598-023-36560-z
https://doi.org/10.3846/aviation.2022.16471
https://web.mit.edu/drela/Public/web/xfoil/
https://stable-baselines3.readthedocs.io/en/master/index.html
https://github.com/as5652/airfoil-design-optimization

## Slide 17: Thank you!